## Slide 1: Got a Drone… Now what? Mapping with your UAV.
August 12, 2020
Kris Berglund
Vice-President, Sales

## Slide 3: Agenda
Lidar point clouds vs photogrammetric point clouds & output derivatives
Flight paths & Loading UAV photos – what’s important to know
Reconstruction of a 3D environment from 2D
Analysis
  PC thinning & classification
  ‘Best Fit’ PC vertical adjustment

## Slide 4: LiDAR Light Detection and Ranging
Aerial Sensors- Aircraft, Helicopter, UAV
  Output Topographic or Bathymetric data
Terrestrial Sensors- Stations, Vehicles, Backpacks
  Hi-res scans, used more for 3D meshes
Credit LiDARUSA/Fagerman Tech.
Credit Ian Dowman
Notes: Lidar diagram Image: Dowman, Ian. (2004). Integration of LiDAR and IFSAR for mapping. International Archives of Photogrammetry and Remote Sensing. 35.

## Slide 6
Figure: From point observation and intrinsic camera parameters, the 3D structure of the scene is computed from the estimated motion of the camera.
© Copyright 2013-2017, OpenMVG
Measuring distance of the same “objects” using multiple overlapping photographs
Better results are achieved with photos that have good texture, contrast, RGB color definition
Photogrammetry Structure from Motion
Notes: Find distinct features, try to match them, then triangulate their position
When the images don’t have the same color, exposure, camera properties, etc. this get more difficult (separate project in CS usually termed Big SFM to deal with these unorganized images, i.e. VGI)
- Flickr, google etc.
http://www.cs.cornell.edu/projects/bigsfm/

## Slide 8: 3D Modeling
Measuring distance of the same “objects” using multiple overlapping photographs
Better results are achieved with photos that have good texture, contrast, RGB color definition
Credit https://blenderartists.org/
Notes: Using historic information
Possibly adding on to or starting from remotely sensed data

## Slide 10: Data Analysis
Defining Flight Path & Loading UAV Photos
Photogrammetric Point Cloud Generation
Manipulation - 3D Modeling – DSM/DTM
Visualization – cross section profiles, cross profiles, best fit adjustment

## Slide 12: Data Analysis
Defining Flight Path & Loading UAV Photos
Photogrammetric Point Cloud Generation
Manipulation - 3D Modeling – DSM/DTM
Visualization – cross section profiles, cross profiles, best fit adjustment

## Slide 14: Data Analysis
Defining Flight Path & Loading UAV Photos
Photogrammetric Point Cloud Generation
Manipulation - 3D Modeling – DSM/DTM
Visualization – cross section profiles, cross profiles, best fit adjustment

## Slide 16: Data Analysis
Defining Flight Path & Loading UAV Photos
Photogrammetric Point Cloud Generation
Manipulation - 3D Modeling – DSM/DTM
Visualization – cross section profiles, cross profiles, best fit adjustment

## Slide 19: Dissemination
3D Web Viewers (Sketchfab, 3DHOP)
Virtual Reality / Augmented Reality / Mixed Reality
  Google 360 video, Google Cardboard
  Unity
  Microsoft HoloLens
Replicas and reproductions
  3D printing
  Simulate repairs or reconstruction after damage
Notes:   http://vcg.isti.cnr.it/3dhop/demo.php#external
  https://archaeologydataservice.ac.uk/archives/view/lascuevas_uchn_2016/viewer.html

## Slide 20: BGC Engineering Case Study Integrated Mine Planning – 2018
Notes: Discovery / Pre-excavated sites
  El Mirador (Example 1)
Damaged or lost sites
  Project Mosul / Rekrei (Example 2)
  Pompeii (Example 3)
  Reconstruction from volunteered photos
General Access and Education
  CyArk (Example 4)
  Zamani Project (Example 5)
  VR / AR
  Replicas
  Accurate maps
  Historical reconstruction

## Slide 23: Thanks and Be Safe!
August 12, 2020
Kris Berglund
Vice-President, Sales